Material Safety Data Sheet

| SECTION I |
| --- |
| IDENTIFICATION OF PRODUCT AND MANUFACTURER INFORMATION |
| SUBSTANCE TRADE NAME | FUEL OIL (BUNKER C) |
| PRODUCT NAME | BUNKER C |
| MANUFACTURER | RECOPE |
| MANUFACTURER ADDRESS | 100 Metros este del Periódico La República. Barrio Tournón, San José, Costa Rica |
| TELEPHONE NUMBER | 2284-2704 y 2284-2745 | FAX NUMER 2255-2049 |  |
| EMERGENCY PHONE NUMBER | 2550-3627 | 2550-3500 |  |
| SECTION II |
| COMPOSITION / INFORMATION ON INGREDIENTS |
| Hazardous Components | % | CAS No. |
| Fuel Oil (bunker C) | 100 | 68553-00-4 |
| Mixture of paraffinic hydrocarbons, olefinic, naphthenic and aromatics including polycyclic aromatic hydrocarbons |  |  |
| SECTION III |
| HAZARDS IDENTIFICATION AND POTENTIAL HEALTH EFFECTS |
| INHALATION | Excessive inhalation of spray or mist may cause irritation of the nose and throat ,respiratory tract, euphoria, cardiac arrhythmia, increased respiration, cyanosis, pulmonary edema, respiratory arrest, kidney damage, affects central nervous and unconsciousness depending on the concentration and exposure time. |
| INGESTION | Ingestion may cause gastrointestinal irritation, vomiting and diarrhea and in severe cases central nervous system depression. |
| EYES | Contact with liquid or concentrated vapor may cause irritation |
| SKIN | May cause skin irritation and blockage of the sebaceous glands resulting in allergies and acne mainly in the hands and fingers. |
| CARCINOGENICITY | IARC lists this product as probable carcinogenic (Group 2B, limited to animal data) . NTP and OSHA not list Fuel Oil as carcinogenic. |
| MUTAGENICITY | No available information |
| TERATOGENICITY | No available information |
| NEUROTOXICITY | No available information |
| OTHERS | No available information |
| TARGET ORGANS | Central nervous system and respiratory tract |
| SECTION IV |
| FIRST AID MEASURES |
| EYE: | Carefully lift the lid and wash continuously with water for at least 15 minutes. Seek medical attention if irritation or discomfort persists. |
| SKIN | Remove contaminated clothing. Wash contaminated areas thoroughly with soap and water or waterless hand cleanser. Obtain medical attention if irritation or redness develops. |
| INHALATION | Remove person to fresh air. If person is not breathing provide artificial respiration. |
| INGESTION | Do not induce vomiting. Do not give anything if the person is unconscious. If the victim presents nauseas, place the head over the kneels to avoid aspiration. Give one or two cups of water if the person is conscious. Seek for medical attention. |
| RECOMMENDED ANTIDOTE | Coal and milk |
| MEDICAL INFORMATION | Treat symptomatically and sustainable overexposure |
| SECTION V |
| FIRE FIGHTING MEASURES |
| FLASH POINT | 60 ºC mínimum |
| LOWER EXPLOSIVE LIMIT | LEL : 3,9 %v/v |
| UPPER EXPLOSIVE LIMIT | UEL: 20,1 % v/v |
| EXTINGUISHING MEDIA | Dry chemical, CO2, water fog, fire fighting foam. Do not use direct stream, because the oil can spread the fire. Cool fire of exposed containers with water spray. |
| PROTECTIVE EQUIPMENT FOR FIRE FIGHTING | In case of FIRE that may result in smoke or toxic by products of combustion should require NIOSH/MSHA approved positive pressure supplied air respirator. |
| HAZARDOUS COMBUSTION PRODUCTS | Toxic and irritating fumes can be produced. |
| SECTION VI |
| MEASURES IN CASE OF SPILL OR LEAK |
| SPILLAGE CARE |
| Notify to the security and emergency personnel . Eliminate all the ignition or heat sources. Do not allow the entrance of nonauthorized personnel. The personnel that participate shall be protected from vapors inhalation and direct contact of skin and eyes. Do not touch or walk through spilled material Do not flush down sewer of drainage systems, basements, confined spaces and river waterways. Immediately soak the product with inert non-combustible material such as diatomaceous earth, sand or oil absorbing materials, using non sparking tools. Place the material in containers with lids suitable for later disposal. After completing the operation ventilate the area and wash spill site. OSHA (29CFR 1910.120) Regulations can be applied. |
| SECTION VII |
| HANDLING AND STORAGE |
| STORAGE TEMPERATURE | Not specified |
| STORAGE CONDITIONS | Keep away from flame, sparks. Store in a well-ventilated area. Avoid storage near incompatible materials . Store in closed containers in a cool, well ventilated areas, away from heat sources, ignition and incompatible substances. |
| CONTAINERS HANDLING | Avoid inhalation of product vapours, fog, skin exposure, eye contact. Handle only with adequate ventilation to reduce levels of hazardous material. Use goggles and appropriate clothing. Remove sources of heat and ignition. |
| EFFECTS OF EXPOSURE TO SUNLIGHT, HEAT, humid atmosphere, ETC. | This product is stable at room temperature, heat, humid atmospheres, etc., in closed containers under normal storage and handling. No hazards are produced by polymerization. |
| SECTION VIII |
| EXPOSURE CONTROLS AND PERSONAL PROTECTION |
| ENGINEERING CONTROLS | Use adequate ventilation to keep vapor concentrations of this product below occupational exposure and flammability limits, particularly in confined spaces. Local extraction systems are preferred to avoid the dispersion of the contaminants in the working areas. |
| RESPIRATORY PROTECTION | Refer to OSHA 29CFR 1910.134, NIOSH Respirator Decision Logic, and the manufacturer for additional guidance on respiratory protection selection. Select the respirator to provide adequate protection to the workers in the workplace, avoiding exposure limits of contamination and oxigen presence. In case of emergency use SCBA systems. |
| EYE PROTECTION | Use safety glasses or chemical safety goggles according OSHA (29CFR 1910.133) regulations. |
| SKIN PROTECTION | Use appropriate clothing including suits, gloves, boots and face mask to provide for prolonged or repeated contact with skin. |
| CONTROL DATA FOR THE EXPOSURE (TLV, PEL, STEL | OSHA PEL: 8 hr. TWA: 500ppm (2000 mg/m3) NIOSH REL 10 hr. TWA: 350mg/m3 |
| SECTION IX |
| PHYSICAL AND CHEMICAL PROPERTIES |
| ODOR AND APPEARANCE | Dark, viscous liquid with characteristic oil odor |
| SPECIFIC GRAVITY | 0,96. @ 15º C |
| SOLUBILITY IN WATER | Insoluble |
| MELTING POINT | -46 ºC |
| BOILING RANGE | > 400 º C |
| AGGREGATE STATE @ 25°C Y 1 ATM. | --------- |
| SECTION X |
| STABILITY AND REACTIVITY |
| STABILITY | Stable under normal ambient temperature under storage and handling conditions. |
| INCOMPATIBLE MATERIALS | The product is incompatible with strong oxidizers. |
| HAZARDOUS POLYMERIZATION | Will not occur polymerization reactions. |
| HAZARDOUS DECOMPOSITION PRODUCTS | Oxidative Thermal decomposition can produce toxic combustion products (eg., oxides of carbon and sulfur) |
| SECTION XI |
| TOXICOLOGICAL PROPERTIES |
| Acute dermal (DL50) | 500 mg (rabbits) results in irritation 5300 mg/kg (rabbits, oral) 5200 mg /kg (rabbits, skin) |
| INHALATIOM LETHAL DOSIS MEDIA (CL50) | Not available |
| SECTION XII |
| ECOLOGICAL INFORMATION |
| Not available |
| SECTION XIII |
| DISPOSAL CONSIDERATIONS |
| Consult federal, state and local waste regulations to determine appropriate disposal options. |
| SECTION XIV |
| TRANSPORT INFORMATION |
| Transport data according DOT) Proper Shipping Name: Fuel Oil Hazard Class : 9 Nº ID : UN 3257 Packing Group: lll Shipping Label: Combustible liquid |
| SECTION XV |
| REGULATORY INFORMATION |
| Classified as Dangerous Product RCRA( 40 CFR 261.21) : prone to ignition Dangerous Number of Residue RCRA : D001 Listed as Dangerous Product CERCLA (40CFR 302.4) : prone to ignition RCRA Sec. 301 Toxic substance SARA (40 CFR 372.65. not listed) OSHA regulations: Listed as air contaminant (29CFR 1910.1000) ; as Oil distillate. SARA Section 311 : Acute Health Hazard Chronic Health Hazard Fire Hazard |
| SECTION XVI |
| OTHER INFORMATION |
| This product is only designed for use as fuel. It can accumulate dangerous concentrations of hydrogen sulfide (H2S) in the storage tanks and reception, the compartments of marine vessels, collecting pits or other confined spaces. By opening the valves, hatches and dome covers, stay upwind, keep face as far away as possible from the opening and avoid breathing any gases or vapors. When exposure concentrations are unknown and no respiratory protection is used, you must use personal devices to warn the presence of H2S. You should not depend on these devices to warn of potentially lethal concentrations. H2S rapidly fatigue the sense of smell. The rotten egg odor of H2S disappears quickly, but still present high concentrations. The TLV / TWA of the ACGIH of H2S is 10 ppm, the limit of short-term exposure (STEL) of the ACGIH is 15 ppm. |