| SECTION I |
| --- |
| IDENTIFICATION OF PRODUCT AND MANUFACTURER INFORMATION |
| SUBSTANCE TRADE NAME | DIESEL |
| PRODUCT NAME | DIESEL (GAS OIL) |
| MANUFACTURER | RECOPE |
| MANUFACTURER ADDRESS | 100 meter East from The República newspaper. Tournón town. |
| TELEPHONE NUMBER | (506) 2284-2745 | FAX NUMER (506) 2255-2049 |  |
| EMERGENCY PHONE NUMBER | (506) 2550-3627 | (506) 2550-3500 |  |
| SECTION II |
| COMPOSITION / INFORMATION ON INGREDIENTS |
| Hazardous Components | % | CAS No. |
| Diesel | 100 | 68334-30-5 |
| SECTION III |
| HAZARDS IDENTIFICATION AND POTENTIAL HEALTH EFFECTS |
| Hazard classification NFPA: Health: 0 flammability: 2 Reactivity: 0 |
| INHALATION | Vapors or mist may cause irritation of the nose and throat ,respiratory tract, euphoria, cardiac arrhythmia, increased respiration, cyanosis, pulmonary edema, respiratory arrest, kidney damage, central nervous system toxicity as a result of inhaling smoke and fumes. |
| INGESTION | Ingestion may cause gastrointestinal disturbances, including irritation, nausea, vomiting and diarrhea and in severe cases other central nervous system effects may result in coma and death. Aspiration may result in severe lung damage. |
| EYES | May cause irritation, experienced as mild discomfort and seen as slight excess redness of the eye. |
| SKIN | May cause skin irritation and blockage of the sebaceous glands resulting in allergies and acne mainly in the hands and fingers. |
| CARCINOGENICITY | IARC lists of occupational exposure in petroleum refining as group 2A (probable carcinogenic to humans (Group 2A) and light distillate group 3 (not carcinogenic to humans). ACGIH listed as TLV-A3 ( carcinogenic animal) . NTP and OSHA not list diesel as carcinogenic. |
| MUTAGENICITY | No available information |
| TERATOGENICITY | No available information |
| NEUROTOXICITY | No available information |
| OTHERS | No available information |
| TARGET ORGANS | Central nervous system and respiratory tract |
| SECTION IV |
| FIRST AID MEASURES |
| EYE: | In case of contact with eyes, inmediately flush with clean water for at least 15 min. Hold eyelids open to ensure adequate flushing. Seek medical attention. |
| SKIN | Remove contaminated clothing. Wash contaminated areas thoroughly with soap and water or waterless hand cleanser. Obtain medical attention if irritation or redness develops. |
| INHALATION | Remove person to fresh air. If person is not breathing provide artificial respiration. |
| INGESTION | Do not induce vomiting. Do not give anything if the person is unconscious. If the victim presents nauseas, place the head over the kneels to avoid aspiration. Give one or two cups of water if the person is conscious. Seek for medical attention. |
| RECOMMENDED ANTIDOTE | No specified. |
| MEDICAL INFORMATION | Gastric lavage is contraindicated because of danger of aspiration. Consider the administration of coal or milk |
| SECTION V |
| FIRE FIGHTING MEASURES |
| FLASH POINT | 52 ºC mínimum |
| LOWER EXPLOSIVE LIMIT | LEL : 1,3 %v/v |
| UPPER EXPLOSIVE LIMIT | UEL: 7,5 % v/v |
| EXTINGUISHING MEDIA | Dry chemical, CO2, water spray, fire fighting foam, fog. Water may be ineffective for extinguishment, unless used under favorable conditions by experienced FIRE fighter. Water spray is recommended to cool or protect exposed materials or structures. |
| PROTECTIVE EQUIPMENT FOR FIRE FIGHTING | In case of FIRE that may result in smoke or toxic by products of combustion should require NIOSH/MSHA approved pressure-demand self-contained breathing apparatus . |
| HAZARDOUS COMBUSTION PRODUCTS | Toxic by products of combustion, carbon oxide and sulphur could be produce. |
| SECTION VI |
| MEASURES IN CASE OF SPILL OR LEAK |
| SPILLAGE CARE |
| Notify to the security and emergency personnel . Eliminate all the ignition or heat sources. Do not allow the entrance of nonauthorized personnel. The personnel that participate shall be protected form vapors inhalation and direct contact of skin and eyes. Do not flush down sewer of drainage systems, unless system is designed and permitted to handle such material. Take up with sand or other oil absorbing and inert materials as diatomaceous earth. Carefully scoop or sweep up into a waste container for reclamation or disposal – caution, flammable vapors closed containers. Wash the place. OSHA (29CFR 1910.120) Regulations can be applied. |
| SECTION VII |
| HANDLING AND STORAGE |
| STORAGE TEMPERATURE | Not specified |
| STORAGE CONDITIONS | Keep away from flame, sparks. Store in a well-ventilated area. Avoid storage near incompatible materials . |
| CONTAINERS HANDLING | Avoid inhalation of product vapours, fog, skin exposure, eye contact. Handle only with adequate ventilation to reduce levels of hazardous material. Use goggles and appropriate clothing. Remove sources of heat and ignition. Ground all containers during transfers to provide for static electricity. Use non-sparking tools to open and close containers. |
| EFFECTS OF EXPOSURE TO SUNLIGHT, HEAT, humid atmosphere, ETC. | This product is stable at room temperature, heat, humid atmospheres, etc., in closed containers under normal storage and handling. No hazards are produced by polymerization. |
| SECTION VIII |
| EXPOSURE CONTROLS AND PERSONAL PROTECTION |
| ENGINEERING CONTROLS | Use adequate ventilation to keep vapor concentrations of this product below occupational exposure and flammability limits, particularly in confined spaces. Local extraction systems are preferred to avoid the dispersion of the contaminants in the working areas. |
| RESPIRATORY PROTECTION | Refer to OSHA 29CFR 1910.134, NIOSH Respirator Decision Logic, and the manufacturer for additional guidance on respiratory protection selection. Select the respirator to provide adequate protection to the workers in the workplace, avoiding exposure limits of contamination and oxigen presence. In case of emergency use SCBA systems. |
| EYE PROTECTION | Use safety glasses of goggles according OSHA (29CFR 1910.133) regulations. |
| SKIN PROTECTION | Use appropriate clothing including suits, gloves, boots and face mask to provide for prolonged or repeated contact with skin. |
| CONTROL DATA FOR THE EXPOSURE (TLV, PEL, STEL | ACGIH TLV. OSHA PEL TWA: 100mg/m3, skin Oil destilates 8 hr. TWA: 500ppm (2000 mg/m3) NIOSH REL IDLH level 10 hr. TWA: 350mg/m3 as oil destilates 1100 ppm. |
| SECTION IX |
| PHYSICAL AND CHEMICAL PROPERTIES |
| ODOR AND APPEARANCE | Clear, yellowish viscous liquid with slightly kerosene odor |
| SPECIFIC GRAVITY | 0,84. @ 15º C |
| SOLUBILITY IN WATER | Negligible |
| MELTING POINT | -34 ºC |
| BOILING RANGE | 150- 370 º C |
| AGGREGATE STATE @ 25°C Y 1 ATM. | --------- |
| SECTION X |
| STABILITY AND REACTIVITY |
| STABILITY | Stable under normal ambient temperature under storage and handling conditions of temperature and pressure. Flammable liquid and vapor. |
| INCOMPATIBLE MATERIALS | React strongly in fluor presence. The product is incompatible with strong oxidizers, halogens, strong acids, alkaline substances. |
| HAZARDOUS POLYMERIZATION | Will not occur polymerization reactions. |
| HAZARDOUS DECOMPOSITION PRODUCTS | Oxidative Thermal decomposition can produce toxic combustion products (eg., oxides of carbon, sulfur and other hydrocarbons. |
| SECTION XI |
| TOXICOLOGICAL PROPERTIES |
| Acute dermal (DL50) | 7500 mg/kg (rats, oral) >5ml /kg (rats, skin) |
| INHALATIOM LETHAL DOSIS MEDIA (CL50) | Rats: 2g/m3/6 hr/3 weeks. Change in erythrocytes count, , y focal fibrosis and other changes in lung, chest and breathing |
| SECTION XII |
| ECOLOGICAL INFORMATION |
| Young shad fish in salt water: 204 mg / L/24hr. , Wild ducks, LD50 = 20 mg / kg You can evaporate the water forming on the surface suspended sediments. Degradation can occur in soil and water |
| SECTION XIII |
| DISPOSAL CONSIDERATIONS |
| Consult federal, state and local waste regulations to determine appropriate disposal options. |
| SECTION XIV |
| TRANSPORT INFORMATION |
| Transport data according DOT (49CFR 172.101) Proper Shipping Name: diesel fuel Hazard Class : 3 Nº ID : UN 1202 Packing Group: lll Shipping Label: Flammable liquid |
| SECTION XV |
| REGULATORY INFORMATION |
| EPA regulations: Classified as Dangerous Product RCRA( 40 CFR 261.21) : prone to ignition Dangerous Number of Residue RCRA : D001 Listed as Dangerous Product CERCLA (40CFR 302.4) : prone to ignition RCRA Sec. 301 Toxic substance SARA (40 CFR 372.65. not listed) OSHA regulations: Listed as air contaminant (29CFR 1910.1000) ; as Oil distillate. |
| SECTION XVI |
| OTHER INFORMATION |
| Information collected by RECOPE Quality Control Dept |